## Slide 1
Investigatory Project
Using Sound to Measure Temperature
Objective
The objective is to determine the temperature of the air inside a pipe by measuring the speed of sound.
Requirements
Microphone
Speaker
Oscilloscope
Audio Generator
Thermometer
Hairdryer
3.6 (3 ft and 7 in) Foot Pipe
Procedure
After placing the speaker and microphone at each end of the pipe, measure the length of the pipe, which is the distance between the speaker and the microphone.
To find the lag time between the speaker input and output for the temperatures from 0 to 100 degrees Celsius, combine the equations: v (sound) =331+0.6T and v=d/t, where d=1.1 meters, and T= temperature in degree Celsius. These two equations would combine to create d/t=331+0.6T.
Calculate the time it takes sound to travel through the pipe at 0(C), and the time it takes sound to travel through the container at 100(C), and subtract them.
Divide this number by a hundred.
Use a hair dryer to heat the air in the pipe to the desired temperature and turn on the sound waves.
Mark the intersection of the wave on the oscilloscope grid before and immediately after the hairdryer has been used. This will indicate the lag time.
Now, for every 5 microseconds of lag, add one degree Celsius.
Calculate the temperature, and compare the number with the thermometer. Wait until the pipe cools down, and then repeat the procedure
Result
After repeating the experiment 10 times, I found out that my calculated and actual temperatures derived from a thermometer differed on average by 2.8(C). My average percent of error was 4.89%.
Summary
We concluded that I was able to accurately predict the temperature by the velocity of the sound that passed through it. Whenever the temperature was increased, the speed increased; conversely, as the air slowly cooled, the speed decreased. I think this is due to the fact that with a higher temperature, more energy is in the air. With more energy, particles are able to vibrate faster, thus increasing the speed of sound.
This project determined the temperature of air by using the fact that temperature has an effect on the speed of sound.
1

## Slide 2
Investigatory Project
Sink or Float
Objective
The objective of this project is to determine the required salt concentration to make an object of varying weights float in three different fluids: tap water, distilled white vinegar, and 7 Up. The goal is to demonstrate Archimedes's principle by showing the effect of salt concentration on fluid density and buoyancy.
Methods / Materials
The materials involved consists of a test container, a plastic container with variable weights, a scale, a floating thermometer, stirring sticks, salt, tap water, distilled white vinegar, and 7 Up.
I conducted tests to determine how much salt is needed for an object to float in each test fluid as the mass of the object is increased.
For each fluid, I started with an object that floats in fresh fluid (no salt) and increased the mass of the object five times, each time by ten grams.
Result
The results clearly show that, as the object mass is increased, more salt is needed to keep the object afloat. Furthermore, vinegar and 7 Up, which are denser fluids, require less salt than water to float an object of the same weight.
Conclusions / Discussions
The experiments demonstrate that the higher the density of any fluid, the greater the mass of the object that can float in it.
In the water experiment, as the object mass is increased, more salt has to be added to the water to increase its density.
The same observations can be made with two other fluids with higher densities than water, vinegar and 7 Up.
As more salt is added to these two fluids, their densities increase, and an object with a greater mass can float in them.
The experiments with vinegar and 7 Up also show that these two fluids can float object with greater mass than tap water, since they have higher densities than water.
This project demonstrates the effect of salt concentration on the density of a fluid and the buoyancy of an object floating in the fluid.
2

## Slide 3
Investigatory Project
Reflections on Reflections
Objective
The purpose of this years science project, Reflections on Reflection, was to attempt to develop a cost effective method of concentrating light onto a photovoltaic solar panel.
Specifically, we tested which reflective materials work well and by how much it improves efficiency. As a result of the low accuracy of the hyperbolic and smaller parabolic reflector, only the large parabolic reflector was used. Our tests include one thirty minute and five ten minute trials with and without using the large parabolic reflector.
Methods / Materials
The procedure included constructing a Cassegrain reflector using mirror tape and window mirror film, and allowing a photovoltaic solar panel to charge three AA Ni-MH batteries for sets of 10 and 30 minutes with and without the use of the reflector.
After the charging period, the cumulative voltage of the batteries was tested and were connected to six LED lights; this duration was recorded.
Five sets of ten minutes and one set of thirty minutes were conducted.
Result
The data supported the idea that such a device can enhance the power of a photovoltaic cell.
In the ten minute period, the batteries charged with the reflector lit the LEDs for 46 minutes, while the batteries charged without the reflector lit the LEDs for an average of 15 minutes.
This shows that using the reflector tripled the charge stored in the batteries under a given time.
Ultimately, voltage did not serve well as a means of measuring how much more energy was absorbed.
Conclusions / Discussions
This experiment produced applicable information that may possibly influence the solar panel industry by providing less expensive CPV solar units. Finding ways to produce an affordable means of manifesting solar light is the major struggle the solar companies face; by continuing and expanding upon experiments like this the use of solar energy will help to win the fight for energy independence.
This project was to see Reflections on Reflections is an exploration of concentrate photovolatics, by constructing a modified Cassegrain reflector.
3